Libraries
1. MemoryFree.h – Check free memory
2. LedControlMS.h – for led display
3. SoftwareSerial.h – Serial communication with 9600 baud wifi module

Functions
1. void setup(void)
2. void setupWifi()
3. void loop(void)
4. void doSwitch()
5. void mintempCheck()
6. void maxtempCheck()
7. void searchIPD(uint8_t input)
8. void handleIPDMessage()
9. void sendToVisitor(String idString, char * pageData)
10. char * servePage(int urlNumber)
11. char *ftoa(char *a, double f, int precision)
12. char * getTempJsonResponse()
13. char * getSuccesJsonResponse(boolean truefalse, char *reason)
14. int tryToSetTempTo(float target)
15. int switchURL(char * url)
16. float stringToInt(String dataLengthString)
17. void scrollLeft(float ch)
18. void DoScrollText()
19. void alarm(int code, byte data[], int index)
20. void watch(int code, byte data[], int index)

Funtion description
void setup(void)
  1. setup pins
  2. reference voltage to 3.3V
  3. begin serials
  4. set variables to first values
  5. setup de display
  6. call setup wifi
2. void setupWifi()
  1. begin serial for wifi
  2. reset the module
  3. set module as accesspoint
  4. set accesspoint name and password
  5. allow multiple connections (fridge not programmed to support that fully)
  6. open a web server
3. void loop(void)
  1. read the temperature and take averages
  2. call doSwitch() to check if the relay should switch
  3. call min and maxtemp checks
  4. call DoScrollText(); to scroll the text 1 position(screendot) to the left
  5. if there is data from the wifi module call searchIPD(); to search for and incoming messenge (IPD)
4. void doSwitch()
  1. check if it’s time to consider a switch – there is only a switch if there has enough time passed – can be set in the variables
  2. check if temperature below or above the switching threshold
  3. if so, switch the relay
  4. if mintemp or maxtemp signal from the functions for these turn relay off